## Slide 1
MECHATRONIC SYSTEMS & ROBOTICS

## Slide 2: Digitbrain experiment. FMUs, Maestro and delay compensators
Three cases are considered:
- Ideal case: it represents a co-simulation using two FMU, or a simulator connected to a testrig testing a prototype of suspension.
- Delayed case: the second model represents same co-simulation, but there is a delay between the simulator and the testrig.
- Simulation with delay and compensation: it includes a predictor and an interpolator to compensate the messages loses or delayed from the quarter car model to the damper test rig.
Some simulations that implement delay and compensation of delay in the transmission of data between the model of quarter car and a testrig testing a suspension are model defined.
Ideal case
Delayed case
Simulation with delay and compensator

## Slide 3: Ideal case.
This SIMULINK simulation works in the ideal case. A model of the external inputs to the car “RoadBody” , a quarter car model and the model of the active damper. The Simulink model is initiated pushing double click the button “INITIALIZE QUARTER CAR”
Ideal case
File: CompleteSimulationBaseCase.xls
¼ car
Damper

## Slide 4: Delayed case
This SIMULINK model shows the behaviour of the model with transmission delay between the simulation and the testrig.
In order to reduce the complexity of the example, only the delay from the simulator to the test rig is defined.
Delayed case
File: CompleteSimulationBaseCaseDelayed.xls
Delay

## Slide 5: Delay and compensation
This SIMULINK model shows the behaviour of the model with transmission delay between the simulation and the test rig. It also includes the delay compensation..
File: CompleteSimulationBaseCaseDelayedCompensated.xls
Simulation with delay and compensator
Predictor
Collector-Interpolator
Sender

## Slide 6: FMUs generated
In order to previous compositions using FMU, five FMUs are generated.
  FMU_QuarterCar
  FMU_Sender
  FMU_Delay
  FMU_Receiver
  FMU_Damper
File: CompleteSimulationBaseCaseDelayedCompensated.xls
FMU_QuarterCar
FMU_Sender
FMU_Delay
FMU_Receiver
FMU_Damper

## Slide 7: FMU_QuarterCar

## Slide 8: FMU_Sender

## Slide 9: FMU Delay

## Slide 10: FMU compilation and composition
This SIMULINK models are compiled for Linux64 target. The FMU can be composed to generate different scenarios.
Delay compensation.
Simulation without delay

## Slide 11: Execution issue
The FMUs have been tested and compared with the FMU equivalent simulation:
- The execution of a simulation with two Simulink blocks of QuarterCar and Damper runs smoothly.
- The execution of the co-simulation with two FMUs simulation stops with a warning of algebraic loop. A memory is necessary to stabilize the simulation.
Memory